## Slide 1: FPGA’s: a new attack surface for embedded adversaries.
John Dunlap

## Slide 2: About Me
@JohnDunlap2
Security Researcher
Reverse Engineer
Avid collector of bad software
Work for GDSSecurity doing code review / RE / Research

## Slide 3: What’s this talk about?
FPGA’s – What are the security concerns?
Also it’s about moving fast, because this is a deep deep topic in a relatively short talk.

## Slide 4: Who is the intended audience?
Security Engineers / Static Analysis People who want to get into FPGAs
Not deep FPGA SME’s, you may not get as much out of this due to time constraints.

## Slide 5: What are FPGAs?

## Slide 6: Field Programmable
You can think of it as a CPU you can reprogram yourself
All of the behaviors of a CPU are yours to define – registers, memory etc..

## Slide 7: Gate Array
Ostensibly an array of Gates.
Not actually, but you are meant to think that way

## Slide 8: In Reality: LUTs (https://electronics.stackexchange.com/questions/169532/what-is-an-lut-in-fpga)

## Slide 9: Most of the time. There are likely deafening sounds of “well actually” in the audience at the moment.

## Slide 10: In reality there are many types of hybrid devices that behave differently.

## Slide 11: FPGA Flavors (This Relevant to Security!)
FPGA’s come in a dizzying variety of types that all behave differently
Different power consumption levels
Different sizes
Different storage methods
Hybrid FPGA/CPLD setups

## Slide 12: FPGA Storage Types
SRAM
Antifuse
PROM
EEPROM
EPROM
Flash

## Slide 13: SRAM

## Slide 14: Static Ram
Boots from a CMOS
Can be easily reconfigured on the fly

## Slide 15: EEPROM

## Slide 16: Flash

## Slide 17: Antifuse FPGA

## Slide 18: But even some antifuse FPGA’s have readback
Trimberger (https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6849432)

## Slide 19: What are people using FPGA’s for?
Everything

## Slide 20: Vehicles without Drivers

## Slide 21: Military Stuff (http://archive.cotsjournalonline.com/articles/view/102372)

## Slide 22: Routers (http://linuxgizmos.com/openwrt-router-sbc-mixes-cortex-a5-and-fpga/)

## Slide 23: Servers

## Slide 24: Of Course

## Slide 25: General Threat Model
Attacks against the hardware itself
Attacks misusing the HDL implementation
Attacks from outside the electronics environment
Attacks against the Synthesis Pipeline

## Slide 26: Hardware is Hard – the intermediate level is even harder
FPGA’s encourage hardware engineers to recapitulate the sins of the last 40 years of computing
FPGA’s are often placed in situations where the data fed to them is intended to be trusted
Security Controls aren’t always the first thought when the device in intended for performance

## Slide 27: Hardware Definition Language
Allows you to program hardware with code
Verilog, VHDL and other proprietary variants
Wires, busses, clocks can be defined dynamically

## Slide 28: HDL Language – Verilog CPU (https://github.com/ejrh/cpu/blob/master/testbench/alu_tb.v)

## Slide 29: Counting Clock Cycles (https://www.edaboard.com/showthread.php?45866-How-to-write-code-in-Verilog-for-skipping-two-clock-cycles-at-a-time)

## Slide 30: The Synthesis Pipeline(http://web.cs.ucla.edu/~miodrag/papers/Majzoobi_2011.pdf)

## Slide 31: Insider Threats May Be an Issue

## Slide 32: Physically Uncloneable Functions
Tie encryption or authentication to device specific factors

## Slide 33: Physically Unclonable Functions

## Slide 34: More

## Slide 35: How would you implement that?
Measuring propagation delays is the typical method
You can also measure voltages, capacitance and other physical factors
Learning Parity with Noise
There are whole books dedicated to getting this right.
These are not perfect, there are attacks.

## Slide 36: These can be defeated by machine learning

## Slide 37: This thesis shows you how (https://github.com/maoswald/cs_masters_thesis)

## Slide 38: https://zzyue.github.io/PUF/ - Great Further Reading List!

## Slide 39: Christoph Boehm is the man when it comes to this topic

## Slide 40: Threat 1: Disclosure of IP
Adversaries will attempt to pull your IP off the board
It has to exist in a form the board will understand and needs to be reloaded on each power on in many situations
The time when you power on the device is most vulnerable

## Slide 41: Methods for Disclosing FPGA IP
Grabbing IP during configuration off of the device
Grabbing IP during boot
Grabbing IP during configuration
Grabbing IP directly off storage

## Slide 42: Bitstream Cloning Attacks
The easiest thing is to abuse the readback functionality of a FPGA where it exists.
Usually a bit can be set to prevent read back, but it’s possible to forget to do this.
Failing this you may have to try and middle the FPGA’s bitstream during boot time. This may be non-trivial.
Encrypted Bitsreams
Integrated Devices

## Slide 43: The Easy Way

## Slide 44: Bitstream Formats
Typically vary from manufacturer to manufacturer
May vary device to device
Almost always proprietary

## Slide 45: Majzoobi puts it well

## Slide 46: Bitstream Encryption

## Slide 47: Some FPGA’s use CBC…

## Slide 48: Bistream Encryption
Key generated by synthesis software
Encrypted at synthesis time
Key later implanted on the device via jtag

## Slide 49: Implementing True Random Numbers In FPGA’s
There are several ways to get true random numbers out of FPGAs
As a security person it may be your job to prove they are in fact random

## Slide 50: FPGA Entropy Sources
These actually end up being similar to the places you get randomness for PUFs
Metastability
Propagation Delay
Oscillator Jitter
Oscillator frequency
Phase Locked Loops
Dedicated hardware peripherals

## Slide 51: Metastability?

## Slide 52: Anti-Tamper Gotchas
Fuses!
Tamper resistant Flash memory cells
Designs which make specific attacks difficult by placement of logic

## Slide 53: Microsemi Smart Fusion – Distributed Storage

## Slide 54: Microsemi FUSELock (https://www.microsemi.com/document-portal/doc_view/129847-ac168-implementation-of-security-in-actel-antifuse-fpgas-app-note)

## Slide 55: Microsemi Flashlock (https://www.microsemi.com/document-portal/doc_view/129931-ac185-implementation-of-security-in-microsemi-proasic-and-proasicplus-flash-based-fpgas-application-note)

## Slide 56: Are the keys secure?

## Slide 57: Xilinx Features

## Slide 58: Xilinx - Antireadback

## Slide 59: ICAP (https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6849432)

## Slide 60: ICAP
Internal configuration port
Makes it possible to rewrite the configuration of the FPGA in the field
Often configured such that the FPGA can rewrite it’s own memory(!)

## Slide 61: Threat 2: Damage to Critical Systems
If a FPGA is connected to a critical system abuse of system logic may be used to cause physical damage to that system
Inappropriate Voltage may be induced to produce a short or an overheating situation

## Slide 62: Existing Research on this topic: http://www.cis.upenn.edu/~jms/papers/fpgavirus.pdf

## Slide 63: They called it MELT!

## Slide 64: What should you look for in your own systems
In much the original research MELT vulnerabilities are created by modifying the bitstream pre-configuration.
This is because in the majority of cases the compiler wont allow the conflicts that are necessary for MELT to occur on the device itself
However, that doesn’t protect peripherals connected to the FPGA. Make sure output voltages are constrained in your designs.

## Slide 65: Threat 3: Attacks Against Hardware of the FPGA itself
You might try to reverse engineer it physically
Focused Ion Beam Measurement ($$$)
Scanning Electron Microscope
Analysis with X-Rays
Thermal analysis

## Slide 66: Threat 3A: Attacks against the FPGA which place it in an unexpected environment
Out of range temperature
Clock Tampering
Voltage tampering
Ionizing Radiation
FIPS140-2, level 4

## Slide 67: Solutions
“Robust Circuitry”
Voltage Regulation
Secure cryptographic implementations
Redundant storage
Use a DAC to implement Shutoffs when temperature is wrong
Physical Isolation of FPGA regions

## Slide 68: Xilinx – Isolation Design Flow

## Slide 69: IDF Visualized (Trimberger/Moore https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6849432)

## Slide 70: “Single Events Upset”
Radiation causes a bit to flip more or less
Happens a lot more in outer space.

## Slide 71: No Really. Space.

## Slide 72: High Level Ideas for Radiation Proofing Your FPGA (https://radhome.gsfc.nasa.gov/radhome/papers/seesym06_berg.pdf)
Good Silicon
“Ultra Low Alpha” materials
“Soft Error Mitigation”
Error Correcting Codes
Design around it
Shield
SRAM

## Slide 73: A Guy At BAE Systems Doing Radiation Hardening Testing

## Slide 74: Threat 4: Shared IP based issues
FPGA’s have libraries too.
Sort of.

## Slide 75: What are IP Blocks?
HDL for your designs provided by 3rd parties.
Often sold by the device manufacturer
Can be as simple as a register and as complex as an entire CPU

## Slide 76: The Intel/Altera IP Blocks Menu

## Slide 77: Threat 5: Cryptographic Attacks
Timing based attacks
Side channel / power analysis
EMF analysis
Fault Injection / Glitch Analysis

## Slide 78: DPA Attacks
Practical for recovering keys and decrypting encrypted bitstreams
May be thwarted by running the circuit in parallel with other power consumers
Still Effective, active area of research

## Slide 79: Timing Analysis
Timing side channels can be used just like a traditional CPU
Constant time algorithms work for this just like on a traditional CPU

## Slide 80: Fault Injection
Voltage starvation
Over Voltage
EMF field
Radiation
Can be counteracted if all states can be accounted for
Or Tamper detection
Not too different from traditional CPUs in all this

## Slide 81: Epilogue: Security Tools For FPGAs

## Slide 82: Static Analysis is Great on FPGA’s!
FPGA’s had cool satisfiability solver technology long before the software industry tried it.
Hardware design was a proving ground for theorem proving based software assurance.
Sadly, most of it is strictly concerned with electrical engineering properties and doesn’t automatically extend to more logical properties of the devices.

## Slide 83: Static Timing Analysis
All toolsets provide a suite to do this prior to configuring the design.
Proves soundness in terms of clock and expected propagation of signals through the design.
Without STA the design might include elements that cause it behave non-deterministicly. Deterministic operations may return differing values.
Each component in the design induces a delay that must be accounted for.

## Slide 84: Issues Finding Security Bugs at the Intermediate Level
STA doesn’t tell you about logical issues in your design.
Questions like “can the user write to arbitrary memory?” are not answered by static timing analysis.
Without your help it cannot harden your crypto against DPA attacks.

## Slide 85: This tool from Cornell is awesome

## Slide 86: Issues a Human Would Find
Bad state transitions
Data flow to unintended areas
“Timing Sensitive Information Flow”
Do critical functions check on the state of the clock?
Race conditions
Synchronous vs asynchronous
(logical) Security modes
Security bit
Aliasing
Memory map issues

## Slide 87: That’s It!
Hope you liked it
I’m @JohnDunlap2 on twitter

## Slide 88: Thanks!